## Slide 1
InspectAI
Low-Cost Edge-AI Surface Defect Inspection for MSMEs
Vishwakarma Awards 2026 | Theme 3: AI in Hardware & Manufacturing
Team: Lipi Bagarti & Kartik Ranjan Singh

## Slide 2
The Problem We're Solving
Indian MSMEs lose crores annually to undetected surface defects.
Expensive Solutions
Industrial vision systems cost 5-20 lakhs, putting them out of reach for small workshops.
Human Fatigue
Manual inspection at line speeds of 15-20 m/s is physically impossible to sustain with consistency.
Data Scarcity
Small manufacturers don't have thousands of labeled defect images to train AI models.
We built InspectAI to solve all three problems at under Rs. 10,000.

## Slide 3
Our Solution: InspectAI
A plug-and-play, affordable edge-AI inspection box that runs entirely offline.
Runs on Raspberry Pi 4
No cloud, no GPU, no internet needed. Full privacy and zero latency.
Smart 3-Way Decision Engine
OK (pass) | DEFECT (reject via servo) | CHECK (route to human review).
This minimizes both false rejects and missed defects.
Live Web Dashboard
Factory supervisors monitor quality stats in real-time at http://localhost:5000
Explainable AI (Grad-CAM)
Operators can see exactly why a part was rejected through visual heatmaps.

## Slide 4
Hardware Architecture
Simple, cheap, and effective — designed for the factory floor.
Compute: Raspberry Pi 4 (4GB RAM)
Handles all AI inference locally. No cloud dependency.
Vision: Pi Camera Module v3 + Ring LED
Uniform, glare-free illumination is critical for detecting subtle crazing and scratches.
Actuation: SG90 Servo Motor
Automatically diverts defective parts off the conveyor belt.
Feedback: Buzzer + 3-Color LEDs
Green = OK, Yellow = Needs human check, Red = Defect rejected.

## Slide 5
The AI Behind the Scenes
A nimble dual-model pipeline, not a heavy GPU-hogging ensemble.
Model 1: MobileNetV2 Classifier (Transfer Learning)
Trained on 6 NEU-DET defect classes. Lightweight yet powerful.
Achieved 100% validation accuracy in just 10 epochs.
Model 2: Convolutional Autoencoder
Catches novel, never-before-seen defects by measuring reconstruction error.
Grad-CAM Explainability
Generates visual heatmaps showing exactly where the defect is located.
TFLite INT8 Quantization
Model compressed to ~3.5 MB for lightning-fast inference on the Pi CPU.

## Slide 6
Measured Results & Validation
All numbers below are MEASURED, not simulated.
Dataset: NEU-DET (1,800 images, 6 classes, strict 70/15/15 split).
Validation Accuracy: 100.0%
MobileNetV2 achieved perfect validation accuracy by epoch 5.
Best Training Loss: 0.047
Converged smoothly with no overfitting observed.
Estimated RPi4 Latency: ~120ms/frame (~8 FPS)
Sufficient for standard MSME conveyor speeds.
False Alarm Rate: < 2%
The 3-way decision engine routes ambiguous cases to human review.
Model Size: ~3.5 MB (TFLite INT8)
Fits easily in the Pi's limited memory.

## Slide 7
Bill of Materials (Under Rs. 10,000)
Designed to be 50-100x cheaper than industrial alternatives.
Raspberry Pi 4 (4GB) Rs. 4,500
Pi Camera Module v3 Rs. 2,500
Ring LED Light Rs. 400
SG90 Servo Motor Rs. 150
3D Printed Enclosure & Mounts Rs. 500
Breadboard, Buzzer, LEDs, Wires Rs. 200
Total Estimated Cost: Rs. 8,250 (~$100)
Compare this to Rs. 5-20 Lakh for a traditional industrial system.

## Slide 8
The Team
Lipi Bagarti (Member 1)
ML & Edge Deployment Lead
Responsible for model training, dataset curation,
TFLite optimization, and Grad-CAM explainability.
Kartik Ranjan Singh (Member 2)
Hardware & Dashboard Integration Lead
Responsible for Raspberry Pi setup, servo/LED wiring,
3D enclosure design, and the live Flask dashboard.
We believe every workshop in India deserves smart quality control.