## Slide 1
VISHWAKARMA AWARDS 2026 · THEME 3
InspectAI: Low-Cost Defect Inspection for MSMEs
AI-powered surface defect detection on an edge device (Raspberry Pi)
Team Member 1: Lipi Bagarti
Team Member 2: Kartik Ranjan Singh

## Slide 2
01 · TITLE OF THE PROJECT
Project at a glance
PROJECT / PRODUCT
InspectAI: Low-Cost Edge-AI Defect Inspection System for MSMEs
THEME
Theme 3: AI in Hardware & Manufacturing
SUB-THEME
Computer Vision & Smart Quality Inspection
SDG ALIGNMENT
SDG 8 (Decent Work and Economic Growth), SDG 9 (Industry, Innovation and Infrastructure)
ANRF ALIGNMENT
Advanced Manufacturing, AI & Robotics, Industry 4.0/5.0 Technologies
TEAM MEMBER 1
Lipi Bagarti
TEAM MEMBER 2
Kartik Ranjan Singh

## Slide 3
02 · PROBLEM STATEMENT
The problem
PROBLEM IN ONE STATEMENT
Small factories inspect parts by eye — slow, inconsistent and unrecorded — because commercial machine-vision systems cost lakhs of rupees.
Slow and tiring
Human eyes tire; defects slip through
Inconsistent
Calls vary from inspector to inspector
No data trail
Defects are not logged or analysed
Too costly to automate
Vision systems are priced for big plants

## Slide 4
03 · SOLUTION PROPOSED · OVERVIEW
An AI inspection box
Place part
Part enters the inspection box
Capture
Fixed LED light + camera take an image
Analyse
Edge AI model runs on the Raspberry Pi
Decide
OK, DEFECT or CHECK, with a confidence score
Act
Servo rejects the part; dashboard logs it
Edge AI, works offline
No cloud or internet needed on the shop floor
Real-time decisions
Target: 5+ frames per second on a Raspberry Pi
Live count and defect log
Simple dashboard: OK / defect count, type and time

## Slide 5
03 · SOLUTION PROPOSED · ARCHITECTURE
System architecture
Hardware layer
Raspberry Pi 4 (edge compute)
Pi camera or USB webcam
LED ring light, enclosed box
IR sensor for part trigger
Servo diverter + buzzer / LEDs
Software layer
Python + OpenCV capture
Image pre-processing
TensorFlow Lite inference
Logic: OK / DEFECT / CHECK
GPIO control of servo, alerts
Data and output layer
SQLite log of every part
Local Flask web dashboard
Counts, defect types, trends
CSV export for reports
Optional Hindi / Odia voice alert

## Slide 6
03 · SOLUTION PROPOSED · AI / ML
Two models, one decision
1. Supervised classifier
Tells us which defect it is
MobileNetV2 or YOLOv8n with transfer learning
Trained on NEU-DET (6 classes, 1,800 images) plus our own photos
Classes: crazing, inclusion, patches, pitted surface, rolled-in scale, scratches
Exported to TensorFlow Lite for the Pi
2. Anomaly detection
Our differentiator
Autoencoder or PatchCore trained on good parts only
Anomaly score = how far a part is from "normal"
Catches new defect types never seen in training
Works for factories that have no defect data

## Slide 7
03 · SOLUTION PROPOSED · PIPELINE
From data to decision
1
Collect data
2
Augment
3
Train
4
Evaluate
5
Convert to TFLite
6
Deploy on Pi
DECISION LOGIC
Model result | Action
Confident DEFECT | Servo rejects part, event logged
Uncertain (between thresholds) | Routed to a human for manual check
Confident OK | Part passes, count logged
HOW WE EVALUATE
Train / validation / test split of 70 / 15 / 15
Accuracy, precision, recall, F1
False-reject rate and inference time
Re-test on our own photos under changed lighting

## Slide 8
03 · SOLUTION PROPOSED · HARDWARE
Low-cost by design
Chart: Estimated bill of materials (Rs)
| Raspberry Pi 4 | Camera module | LED ring light | Servo + IR + buzzer | Box and wiring
Cost (Rs) | 4500 | 800 | 400 | 350 | 950
~ Rs 7,000
estimated prototype cost
Commercial machine-vision systems typically run into lakhs of rupees.
Costs are approximate and will be confirmed at purchase.

## Slide 9
04 · IMPLEMENTATION PLAN
Who benefits, what we deliver
Target beneficiaries
MSME workshops, small foundries and fabrication units
Quality-control inspectors and supervisors
Small manufacturers who cannot afford lakh-range vision systems
Deliverables
Working InspectAI prototype (box, camera, Pi, servo)
Trained model files and dataset notes
Local dashboard and CSV reports
Test report and setup guide
Expected outcomes
Faster, more consistent inspection
Fewer defective parts reaching customers
A defect data trail for process improvement
Lower inspection cost for small units

## Slide 10
04 · IMPLEMENTATION PLAN
Build plan and real-world pilot
W1
Data + baseline model
Get NEU-DET, train the classifier, set up the anomaly model
W2
Box + our own photos
Build the light box, mount the camera, collect 100-200 real images
W3
Deploy on the Pi
Convert to TFLite, wire IR trigger, servo diverter and dashboard
W4
Test + report
Measure accuracy, false-reject rate and speed; prepare demo
REAL-WORLD PILOT
1
Find a partner
A local foundry or fabrication unit for a trial
2
Run side by side
Compare InspectAI with manual inspection
3
Refine and hand over
Tune thresholds, train staff, collect feedback

## Slide 11
04 · IMPLEMENTATION PLAN
Team and responsibilities
TEAM MEMBER 1
Lipi Bagarti
Dataset preparation and augmentation
Model training (classifier + anomaly)
Evaluation and threshold tuning
TEAM MEMBER 2
Kartik Ranjan Singh
Hardware assembly: box, camera, servo
Raspberry Pi integration and deployment
Dashboard and data logging
Shared by both: proposal, testing, documentation and the final demo.

## Slide 12
05 · SAFETY AND EFFICIENCY ANALYSIS
How the solution stays safe
Fail-safe by design
Uncertain parts go to a human; they are never silently passed
Less manual handling
An automatic diverter sorts rejects, so inspectors touch fewer parts
Less eye strain
A clear verdict replaces hours of staring at surfaces
Electrically safe
Low-voltage components inside an enclosed box
Guarded moving part
Only the small reject servo moves, kept behind a guard
Data stays local
Images are processed and stored on the device, with no cloud upload

## Slide 13
05 · SAFETY AND EFFICIENCY ANALYSIS
How it improves efficiency
< 1 s
decision per part
5+ FPS
on a Raspberry Pi
90%+
target accuracy on test set
~Rs 7k
prototype cost
DESIGN TARGETS, TO BE VALIDATED IN TESTING
Automatic reject diversion replaces manual sorting of good and bad parts (material handling)
The same decision quality on every part, all shift, with no fatigue drop
A live defect log lets supervisors fix the process sooner, so fewer bad batches
Inspectors are freed for higher-value tasks such as root-cause checks

## Slide 14
06 · SCALABILITY AND FUTURE DEVELOPMENT
Grow in three phases
Phase 1: Prototype
One part type
Hand-fed tray
Pi + camera + reject servo
Phase 2: Shop floor
Motorised conveyor
Swap models for new parts
Multiple camera angles
Phase 3: Platform
Cloud dashboard and trends
Hindi / Odia voice alerts
Link with predictive maintenance
ADAPTS TO NEW USE CASES BY RETRAINING THE MODEL
PCB solder defects
Bottle caps and seals
Ceramic tiles and glass
Textile and fabric flaws
Fasteners and castings

## Slide 15
07 · INNOVATION ADVANTAGE
Why this is different
 | Manual inspection | Commercial vision | InspectAI
Upfront cost | Low | High (lakhs) | Low (~Rs 7k)
Consistent, all shift | No | Yes | Yes
Works offline | n/a | Vendor-dependent | Yes (edge AI)
Needs defect samples | n/a | Usually yes | No (anomaly model)
Logs defect data | No | Yes | Yes
Learns "good" only
Catches unseen defects without defect samples
Built for MSMEs
Under ~Rs 10k, offline, simple dashboard
Swap-a-model design
Same box adapts to new parts by retraining

## Slide 16
08 · VISUAL IMPACT AND USER JOURNEY
Before and after: the inspector's journey
BEFORE
AFTER
Part arrives
Parts pile up at the inspection table
Part is placed under the camera in the light box
Inspection
Inspector checks each part by eye, hour after hour
Camera + AI check in under a second (target)
Decision
Judgement varies; small defects get missed
Clear OK / DEFECT / CHECK verdict; rejects are diverted
Record
Rarely written down; problems found late
Every part logged; dashboard shows defect trends

## Slide 17
AI quality inspection, within reach of every small factory.
Low cost: ~Rs 7k
Edge AI: works offline
Anomaly detection: no defect samples
Thank you
Lipi Bagarti · Kartik Ranjan Singh