## Slide 1
InspectAI: Bringing Smart Defect Inspection to Every Workshop
Vishwakarma Awards 2026 - Theme 3: AI in Hardware & Manufacturing Team: Lipi Bagarti & Kartik Ranjan Singh

## Slide 2
The Real Problem MSMEs Face
Small manufacturers struggle with quality control. Relying on human eyes to spot tiny defects on fast-moving parts is slow, tiring, and error-prone.
Why not automate? Current industrial vision systems are incredibly expensive, complex to set up, and require massive datasets that small workshops just don't have. We're changing that.

## Slide 3
Our Solution: InspectAI
Meet InspectAI—an affordable, plug-and-play edge AI inspection box.
• Runs completely offline on a low-cost Raspberry Pi.
• Smart 3-way decision engine: Passes good parts, rejects known defects, and flags ambiguous cases for a quick human check.
• Live Dashboard: Track quality in real-time.
Try our live edge dashboard at: http://localhost:5000

## Slide 4
Hardware That Makes Sense
We kept the hardware simple, cheap, and effective:
• Brains: Raspberry Pi 4 (4GB) handles all the AI processing locally.
• Eyes: A standard Pi Camera Module paired with a ring LED for perfect, glare-free lighting.
• Action: A simple 5V servo motor automatically diverts defective parts off the line.
• Alerts: Visual LEDs and a buzzer keep operators informed instantly.

## Slide 5
The AI Behind the Scenes
Instead of heavy, slow models, we built a nimble dual-AI pipeline:
• The Classifier: A lightweight MobileNetV2 model spots known defects like scratches and pits.
• The Anomaly Detector: An Autoencoder catches weird, never-before-seen defects by recognizing when a part doesn't look 'normal'.
• Explainable AI: Our system generates heatmaps (Grad-CAM) so operators can see exactly why a part was rejected.
Everything is quantized to TFLite for lightning-fast speeds on the Pi.

## Slide 6
Proven Results & Validation
We rigorously tested our system on the NEU-DET steel defect dataset with a strict 70/15/15 split.
• Accuracy you can trust: 96.4% overall accuracy with a 95.8% F1 score.
• Fast enough for the line: Processes frames in ~120ms (around 8 frames per second).
• Minimal false alarms: Less than 2% false reject rate, saving good parts from the scrap bin.

## Slide 7
Affordable Bill of Materials
Quality inspection shouldn't cost a fortune. Our prototype costs roughly ₹8,250 (under $100).
• Raspberry Pi 4: ₹4,500
• Pi Camera: ₹2,500
• Lighting, Servo, and Enclosure: ₹1,050
• Electronics (Buzzer, Wires, LEDs): ₹200
This is a fraction of the cost of traditional lakh-rupee systems.

## Slide 8
The Team
We are passionate about bringing accessible AI to the manufacturing floor.
• Lipi Bagarti (Member 1)
Lead on Machine Learning, dataset optimization, and Edge AI deployment.
• Kartik Ranjan Singh (Member 2)
Lead on Hardware integration, custom enclosure design, and the live web dashboard.